## Slide 1: Discrete Fourier transform (DFT)
DFT is used in approximating the spectrum for a finite length sequence.
DTFT is good for theoretical spectrum analysis of digital signal but not good for computer-aided analysis.
DFT provides practical approach to numerical computation of DTFT for a finite length sequence.
Also, we may split an input signal in sets of N samples and do analysis for each set (segment or frame) separately.

## Slide 2: DFT continued
Approximation to X(Ω) is obtained by taking frequency samples of X(Ω) at N equally spaced frequencies Ωk = 2πk / N, 0 ≤ k ≤ N − 1.
Check that the DFT expression is somewhat same as the DTFS expression.
That means, we do analysis in the DTFS manner.
That is, for a given set of N samples we calculate the DTFT as if the signal is periodic with these N samples.
Therefore, one-dimensional DFT and inverse DFT expressions are same as DTFS expressions given before.

## Slide 3: Sampling in frequency
Discuss frequency sampling in the light of what we have studied in case of time sampling at Nyquist rate.
For better approximation we may go for M-point DFT (M > N), as if taking an M-length sequence created by zero padding to the given N-length sequence – discuss in the light of time sampling at a rate greater than Nyquist rate.
N-length sequence
Freq. continuous Spectrum
from −π to +π
Discrete-frequency spectrum
Periodic signal with period N
DTFT
DFT
Freq. sampling
DTFS
Periodic repetition

## Slide 4: Signal recovery from DFT
Given a non-periodic sequence x[n] of whatever length.
We take DTFT and then do frequency sampling at N-points to get DFT coefficients.
x[n] – DTFT  X(Ω) – N-point freq. sampling  X[k]
X[k] = X(Ω = 2kπ/N )
Now we take inverse DFT (expression similar to inverse DTFS) to get back the original signal.
But, we may or may not get back x[n].
X[k] – IDFT 

## Slide 5: Signal recovery from DFT

## Slide 6: Signal recovery from DFT

## Slide 7: Signal recovery from DFT
x[0], x[1], …, x[N-1], x[N], x[N+1] …, x[2N-1], …
DTFT sampling ⇓ and IDFT
(x[0] + x[N] + …), (x[1] + x[N+1] + …),
…, (x[N-1] + x[2N-1] + …), …
(i.e., every Nth sample in x[n] are added up)

## Slide 8: Signal recovery from DFT
Also, check that = for any integer k.
That means, is a periodic sequence with period N.
Since IDFT is somewhat same as inverse DTFS, this is quite expected.

## Slide 9: Signal recovery from DFT
So, how to determine from x[n] directly?
  Split the sequence x[n] into small segments of length N each.
  Add all the segments to get an N-length sequence.
  is the periodic repetition of this N-length sequence.
  However, we only write down the values of these for n = 0 to N−1 as it is unnecessary to repeat the same.

## Slide 10: Signal recovery from DFT (contd.)
For x[n] of length equal to or less than N, x[n] can be recovered from .
  If length of x[n] is N, then one-period of = x[n]
  Example: x[n] = {2, 3, 8, 1} where N = 4
  Essentially, x[n] = {…, 0, 0, 0, 2, 3, 8, 1, 0, 0, 0, 0, …}, where red colored sample corresponds to x[0].
  So, one-period of = {2, 3, 8, 1}
  If length of x[n] is less than N (say L < N), then one-period of = x[n] padded with (N − L) zeros.
  Example: x[n] = {2, 3, 8} while N = 4

## Slide 11: Signal recovery from DFT (contd.)
  Essentially, x[n] = {…, 0, 0, 0, 2, 3, 8, 0, 0, 0, 0, 0, …}, where red colored sample corresponds to x[0].
  So, one-period of = {2, 3, 8, 0}
If length of x[n] greater than N, there is time-domain aliasing and x[n] cannot be recovered from .
  Example: x[n] = {2, 3, 8, 1, 4, 3} while N = 4
  Essentially, x[n] = {…, 0, 0, 0, 2, 3, 8, 1, 4, 6, 0, 0, …}, where red colored sample corresponds to x[0].
  So, one-period of = {2, 3, 8, 1} + {4, 6, 0, 0}
  = {6, 9, 8, 0}

## Slide 12: Correspondence to Sampling Theorem
Continuous-time periodic signal in time domain ⇌ discrete-frequency non-periodic spectrum (FS coeff’s)
In the same way, continuous-frequency periodic spectrum X(Ω) in frequency domain ⇌ discrete-time non-periodic signal x[n].
Time domain signal sampled with time-interval Ts ⇌ frequency domain spectrum gets repeated after every 2π / Ts = 2πfs = ωs rad / sec
Similarly, frequency domain spectrum X(Ω) sampled at N points with frequency-interval 2π/N rad. ⇌ time domain signal gets repeated after every = N samples.

## Slide 13: Correspondence to Sampling Theorem
According to sampling theorem, ωs ≥ total band-width of spectrum in rad/sec (incl. both pos. and neg. sides of the frequency band) is required for exact reconstruction of the original signal from the time-domain samples.
Similarly, here we require N ≥ total length of signal for exact recovery of the original signal from the frequency-domain samples (DFT coefficients), as checked before.
For ωs > spectrum band-width (in rad/sec), we get a guard-band in between the repeated spectrum repetition.
Similarly, for N > signal length L, we get a guard-time in between the sequence x[n] repetition given by the zero padding of length N−L, as mentioned before.

## Slide 14: Correspondence to Sampling Theorem
That is why, for an N-length sequence we generally do N-point DFT / IDFT.
However, we may go for N-point DFT even for an L-length sequence (L < N). The same has been said before that for an N-length sequence, we may go for M-point DFT (M > N) for better approximation of the spectrum.
We will discuss soon that this more-point DFT / IDFT is also required for carrying out convolution via multiplication in frequency domain – multiplying DFT coefficients and then taking IDFT of these DFT coefficient products.

## Slide 15: Correspondence to Sampling Theorem
For ωs < spectrum band-width (in rad/sec), we get aliasing due to spectrum overlap.
In a similar fashion, for N < signal length L, we get overlapping of the sequences where the last L−N samples in the sequence x[n] gets added with the first L−N samples of the sequence. This is aliasing in time, as discussed earlier with an example.
Another example: x[n] = {2, 3, 8, 1, 4, 3, 5, 7, 2} and we do 4-point DFT followed by 4-point IDFT (i.e. N = 4)
Then, one-period of the IDFT result = {8, 6, 13, 8}

## Slide 16: DFT properties
Linearity:
Circular shift:
denotes circularly shifted by samples.
What do you mean by circular shift?
  is finite-length sequence of length N.
  But, DFT is essentially DTFS of the periodic repetition of which is .
  That is, we can say when linearly shifted by samples towards right.

## Slide 17: DFT properties
  How can we express in terms of ?
  Write the N samples of on a circle; our convention is to write in anti-clockwise direction for increasing n.
  Shift (rotate) the samples in the same anti-clockwise direction corresponding to linear right-shift of .

## Slide 18: DFT properties
What is ?
  = ⇒ First circularly shift clockwise by positions, followed by scaling by −1, i.e. reverse the order about the origin on the circle.
  See for N = 6 and = 2 case
What is ?
  =

## Slide 19: DFT properties
Symmetry:
  For real x[n]: (conjugate symmetry)
  But DFT defined only for k = 0 to N−1
Therefore,

## Slide 20: DFT properties
  That is,
  N
  For imaginary x[n]: N
  (conjugate anti-symmetry)

## Slide 21: Convolution
Case 1: Both and are periodic
  with same period N.
  With different periods N1 and N2
Case 2: periodic with period N but non-periodic of length L.
  N ≥ L
  N < L
Case 3: Both and are non-periodic of lengths N1 and N2

## Slide 22: Circular Convolution
Both and are periodic with same period N –
In general,
  Reflect to get  multiply and add to get
  Shift by n samples towards right for positive n and towards left for negative n to get  multiply and add to get .

## Slide 23: Circular Convolution
So, we observe two facts:
  Taking summation over to will give each infinite valued since both and are of infinite duration (system with periodic is unstable).
  Output is also periodic with same period N.
Therefore, in this case we calculate convolution over one period only to get one period of , denoting as .
Now, since periodic, this can be done more conveniently in a circular arrangement rather than linear convolution.

## Slide 24: Circular Convolution
  Arrange in anti-clockwise, and then arrange clockwise to get ; and denote only one period of and and so of finite length N each.
  Multiply point-to-point and add to get
  Shift by n samples anti-clockwise, n = 1 to N−1, to get . Multiply and add to get

## Slide 25: Circular Convolution
This way of doing convolution is called N-point circular convolution, denoted as
while the general convolution may be specifically called
linear convolution or simply convolution.
As we understand now, circular convolution is applied in convolving two periodic signals, but taking only one period of each.
Now, how to do the same in the frequency domain?

## Slide 26: Circular Convolution
Recall DTFS property:
⇒ = IDTFS
Now, for the same input sequence DFT coefficients = DTFS coefficients, i.e.,
And, for same input coefficients set IDTFS = IDFT
So, we may also find from DFTs of and .

## Slide 27: Circular Convolution
= IDTFS
= IDFT
= IDFT
= IDFT = IDFT
⇒ = are the DFT coefficients of .
Therefore, to perform periodic convolution of two periodic sequences of same period N, take N-point DFTs of one period of each, multiply the DFT coefficients and then take N-point IDFT to get N-length .

## Slide 28: Periodic Convolution
Input periodic sequences and both having same periodicity N
Extract one period and of the input sequences both of length N
N-point circular convolution
N-point DFT, multiply and IDFT
Obtain one period of length N of the periodically convolved sequence
Periodic repetition of with period N to obtain final convolved sequence
Periodic convolution
DTFS and inverse DTFS

## Slide 29: Convolution Property
Convolution property of DFT that stems out from here
(N-point DFT)
for any finite-length sequences and .
So, summarizing the convolutional properties:
  FS: one period , T = period
  FT:
  DTFT:
  DTFS: one period, N = period
  DFT:

## Slide 30: Convolution Property
Taking N-point DFT of finite-length sequences and followed by multiplication of the DFT coefficients and then taking IDFT essentially converts the sequences as if they are both periodic with the same period N and then we do periodic convolution of them.
For computing N-point circular convolution of two sequences of whatever lengths via DFT / IDFT, we have to take same N-point DFT for both sequences since we do point-to-point multiplication of DFT coefficients.
  The value of N needs to be chosen judiciously as we have seen earlier that there is a possibility of time-aliasing after we take IDFT.

## Slide 31: Circular Convolution contd.
Observe that for doing circular convolution, both the sequences must be of same length since we are doing point-to-point multiplication (this is not a necessary condition in linear convolution).
  Both sequences must be of length N to apply N-point circular convolution on them.
  If not we have to do something appropriate to make them equal length sequences.
  In the case discussed we have taken both sequences of same periodicity and so there was no problem.
  Now we will take up other cases.

## Slide 32: Circular Convolution contd.
Both and are periodic but with different periods N1 and N2 –
  Take N = LCM (N1, N2)
periodic with period N and non-periodic with length L, where N ≥ L –

## Slide 33: Circular Convolution contd.
Here again is periodic with period N.
But, unlike the case of both and periodic sequences, here each is finite-valued (system with finite-length impulse response is stable)
One period of can be computed by doing N-point circular convolution; for N > L, length of extended by zero-padding.
Alternatively, perform N-point DFT / IDFT.
  Essentially gives periodic convolution of with periodic repetition of padded with N − L zeros.
  Since N ≥ L there is no question of time-aliasing.

## Slide 34: Circular Convolution contd.
periodic with period N and non-periodic with length L, where N < L –

## Slide 35: Circular Convolution contd.
So, here also one period of can be computed by doing N-point circular convolution. Since, length of is more than N, is time-aliased as follows.

## Slide 36: Circular Convolution contd.
Alternatively, perform N-point DFT / IDFT.
  Taking N-point DFT of finite-length may be thought of as if is periodically repeated with period N.
  But, since length L of is more than the number of DFT points N, there is time-aliasing in the periodically repeated sequence. This is desired since we want circular convolution of with time-aliased as seen above.
  Thus, DFT / IDFT approach essentially gives periodic convolution of with periodic repetition of time-aliased with period N, as desired.

## Slide 37: Circular Convolution contd.
Both and are non-periodic of lengths N1 and N2 –
  Convolution of two non-periodic signals gives a finite-length non-periodic output; the length of the output is N1 + N2 − 1.
  Convolution here is obtained by linear convolution.
  This can only be computed via frequency domain using DTFT / IDTFT.
However, our objective is to do the same via DFT / IDFT since DTFT / IDTFT cannot be performed in a digital processor.

## Slide 38: Circular Convolution contd.
But, we have seen that DFT / IDFT gives circular convolution and not linear convolution.
How is circular convolution related to linear convolution?

## Slide 39: Circular Convolution contd.
Now, we compare this linear convolution to N-point circular convolution for different values of N.
So, for N = 8,
circular convolution
= linear convolution

## Slide 40: Circular Convolution contd.
Now, we compare this linear convolution to N-point circular convolution for different values of N.
So, for N = 6,
circular convolution
= linear convolution

## Slide 41: Circular Convolution contd.
Now, we compare this linear convolution to N-point circular convolution for different values of N.
So, for N = 5,
circular convolution
= +, , , ,

## Slide 42: Circular Convolution contd.
Now, we compare this linear convolution to N-point circular convolution for different values of N.
So, for N = 4,
circular convolution
= +, +, ,

## Slide 43: Circular Convolution contd.
For M ≠ N, N-point circular convolution is different from M-point circular convolution.
Circular convolution can be derived from linear convolution as linear convolution + time-aliasing. That is,
  = one period of
  On the other hand, y[n] can be obtained from circular convolution if there is no time aliasing. And, to avoid time aliasing, N ≥ N1 + N2 − 1.
Thus, linear convolution of two finite length sequences can be obtained via DFT / IDFT if N is taken as above.

## Slide 44: Summarizing
Both and are periodic with same period N (or N = lcm[N1, N2] ): General linear convolution not valid; compute one period of periodic convolution
  via N-point circular convolution of and .
  via N-point DFT / IDFT of and .
  via linear convolution followed by time-aliasing – perform linear convolution giving output sequence of length 2N − 1, then overlap last N − 1 output samples with the first N − 1 output samples resulting in the required N-length one period of the periodic convolution.

## Slide 45: Summarizing
periodic with period N but is of finite-length L: Compute one period of linear convolution
  via N-point circular convolution of and ; for L = N, = , for L < N, is zero-padded and for L > N, is time-aliased to make N-length long.
  via N-point DFT / IDFT of and .
  via linear convolution followed by time-aliasing.
  Note that here taking the convolution sum over to is as good as taking the sum over finite length L. So, here circular convolution gives one period of the actual linear convolution .

## Slide 46: Summarizing
Both and are non-periodic of lengths N1 and N2: Compute Linear convolution computed
  via linear convolution as usual.
  via N-point circular convolution of and , where we take N ≥ N1 + N2 − 1.
  via N-point DFT / IDFT of and .